## Slide 1: Revisiting Hardware-Assisted Page Walks for Virtualized Systems
Jeongseob Ahn, Seongwook Jin, and Jaehyuk Huh
Computer Science Department
KAIST

## Slide 2: System Virtualization
Widely used for cloud computing as well as server consolidation
Hypervisor serves resource managements
  E.g.,) CPU, Memory, I/O, and etc
Hypervisor
OS
App
OS
App
VM1
Virtual
Physical
System
VM2
Virtual
Physical

## Slide 3: Address Translation for VMs
Virtualization requires two-level address translations
  To provide isolated address space for each VM
Guest page tables are used to translate gVA to gPA
Nested
Page Table
(per VM)
System Physical
Address
Guest
Page Table
(per process)
Guest Virtual
Address
Guest Physical
Address
Guest physical address
Offset
gPPN
Page table
Guest virtual address
Offset
gVPN

## Slide 4: Does it make sense ?
Memory required to hold page tables can be large
  48-bit address space with 4KB page = 248/212 = 236 Pages
  Flat page table: 512GB (236 x 23= 239)
  Page tables are required for each process
Multi-level page table
47
offset
VPN
11
0
236
212
VA:
L1
offset
L2
L3
L4
Base address
(CR3)

## Slide 5: Address Translation for VMs
Virtualization requires two-level address translations
  To provide isolated address space for each VM
Current hardware page walker assumes the same organization for guest and nested page tables
  AMD Nested paging
  Intel Extended Page Table
Nested
Page Table
(per VM)
System Physical
Address
Guest
Page Table
(per process)
Guest Virtual
Address
Guest Physical
Address

## Slide 6: Hardware-Assisted Page Walks
Two-dimensional page walks for virtualized systems
gL4
5
gL3
10
gL2
15
gL1
20
gCR3
gVA
Guest page table
(gLn)
nL4
6
nL3
7
nL2
8
nL1
9
nL4
11
nL3
12
nL2
13
nL1
14
nL4
16
nL3
17
nL2
18
nL1
19
nL4
21
nL3
22
nL2
23
nL1
24
sPA
nL4
1
nL3
2
nL2
3
nL1
4
nCR3
gPA (gL4)
sPA
gVA: guest virtual address
gPA: guest physical address
sPA: system physical address
Nested page table
(nLn)
x86_64

## Slide 7: Hardware-Assisted Page Walks
Two-dimensional page walks for virtualized systems
gL4
5
gL3
10
gL2
15
gL1
20
gCR3
gVA
Guest page table
(gLn)
nL4
6
nL3
7
nL2
8
nL1
9
nL4
11
nL3
12
nL2
13
nL1
14
nL4
16
nL3
17
nL2
18
nL1
19
nL4
21
nL3
22
nL2
23
nL1
24
sPA
nL4
1
nL3
2
nL2
3
nL1
4
nCR3
gPA (L4)
sPA
gVA: guest virtual address
gPA: guest physical address
sPA: system physical address
Nested page table
(nLn)
x86_64
Guest (m-levels) and nested (n-levels) page tables
# of page walks: mn + m + n
x86_64: 4*4 + 4 + 4 = 24
Can we simplify the nested page tables ?

## Slide 8: Revisiting Nested Page Table
# of virtual machines < # of processes
  There are 106 processes in a Linux system after booting
Differences address space between VMs and processes
Virtual machines use much of the guest physical memory
  Processes use a tiny fraction of virtual memory space
47
offset
gVPN
11
0
Guest virtual address space
48bit
31
offset
gPPN
11
0
Guest physical address space
e.g.) 32bit (4GB VM)
47
<
Exploit the characteristics of VM memory management

## Slide 9: Revisiting Nested Page Table
# of virtual machines < # of processes
  There are 106 processes in a Linux system after booting
Differences address space between VMs and processes
Virtual machines use much of the guest physical memory
  Processes use a tiny fraction of virtual memory space
47
offset
gVPN
11
0
Guest virtual address space
48bit
31
offset
gPPN
11
0
Guest physical address space
e.g.) 32bit (4GB VM)
47
<
Exploit the characteristics of VM memory management
Multi-level nested page tables are not necessary!!

## Slide 10: Flat Nested Page Table
Reduces the number of memory references for nested page walks
Guest physical address
Offset
gPPN
Flat nested page table
Base address
(nCR3)
Physical memory

## Slide 11: Flat Nested Page Table
Memory consumption
 | Process | Virtual Machine (4GB)
# of pages | 248 / 4KB = 68,719,476,736 | 232 / 4KB = 1,048,576
Flat Page table size | # of pages x 8B = 512GB | #of pages x 8B = 8MB

## Slide 12: Page Walks with Flat Nested Page Table
gL4
5
gL4
10
gL4
15
gL4
20
gCR3
gVA
Guest page table
nL4
6
nL3
7
nL2
8
nL1
9
nL4
11
nL4
1
nL3
2
nL2
3
nL1
4
nL4
12
nL4
13
nL4
14
nL4
16
nL4
17
nL4
18
nL4
19
nL4
21
nL4
22
nL4
23
nL4
24
nCR3
sPA
gPA
sPA
Nested page table
gL4
2
gL4
4
gL4
6
gL4
8
gCR3
gVA
Guest page table
nL4
3
nL4
5
nL4
1
nL4
7
nL4
9
nCR3
sPA
gPA
Nested page table
Reducing 15 memory references from current 24 references

## Slide 13: Does it make sense ?
Flat nested table cannot reduce # of page walks for guest page tables
  It still requires 9 memory references
We would like to fetch a page table entry by a single memory reference
?
Guest Virtual
Address
System Physical
Address
Traditional inverted page table can do it !!

## Slide 14: Traditional Inverted Page Table
Provides direct translation from guest to physical pages
Virtual address
Offset
VPN
Inverted Page Table
(per system)
Physical frames
P-ID
VPN
Hash Key
Hash()

## Slide 15: Inverted Shadow Page Table
Offset
VPN
Guest virtual address
Inverted Page Table
(per system)
Physical frames
P-ID
VPN
Hash Key
Hash()
VM-ID
Nested
Page Table
(per VM)
System Physical
Address
Guest
Page Table
(per process)
Guest Virtual
Address
Guest Physical
Address
Inverted shadow page table

## Slide 16: Inverted Shadow Page Table
Offset
VPN
Guest virtual address
Inverted Page Table
(per system)
Physical frames
P-ID
VPN
Hash Key
Hash()
VM-ID
Nested
Page Table
(per VM)
System Physical
Address
Guest
Page Table
(per process)
Guest Virtual
Address
Guest Physical
Address
Inverted shadow page table
Whenever guest page table entries change,
the inverted shadow page table must be updated

## Slide 17: Inverted Shadow Page Table
1: ...
2: ...
3: update_page_table_entries()
4: ...
1: static int sh_page_fault(...)
2: {
3: ...
4: sh_update_page_tables()
5: ...
6: return 0;
7: }
Guest OS
Hypervisor
Intercepts on page table
edits, CR3 changes
L1
offset
L2
L3
L4
Guest CR3
Guest virtual address
Offset
VPN
Guest virtual address
Inverted Page Table
(per system)
Physical frames
P-ID
VPN
Hash Key
Hash()
VM-ID

## Slide 18: Inverted Shadow Page Table
1: ...
2: ...
3: update_page_table_entries()
4: ...
1: static int sh_page_fault(...)
2: {
3: ...
4: sh_update_page_tables()
5: ...
6: return 0;
7: }
Guest page tables
by guest OS
Shadow page tables
by hypervisor
Intercepts on page table
edits, CR3 changes
L1
offset
L2
L3
L4
Guest CR3
Guest Virtual address
Offset
VPN
Guest Virtual address
Inverted Page Table
(per system)
Physical frames
P-ID
VPN
Hash Key
Hash()
VM-ID
To sync between guest and inverted shadow page table, a lot of hypervisor interventions are required

## Slide 19: Overheads of Synchronization
  Significant performance overhead [SIGOPS ‘10]
  Exiting from a guest VM to the hypervisor
  Polluting caches, TLBs, branch predictor, prefetcher, and etc.
Hypervisor intervention
  Whenever guest page table entries change, the inverted shadow page table must be updated
  Similar with traditional shadow paging
    [VMware Tech. report ‘09] [Wang et al. VEE ‘11]
Performance behavior (Refer to our paper)

## Slide 20: Speculatively Handling TLB misses
We propose a speculative mechanism to eliminate the synchronization overheads
  SpecTLB first proposed to use speculation to predict address translation [Barr et al., ISCA 2011]
  No need for hypervisor interventions, even if a guest page changes
Inverted shadow page table may have the obsolete address mapping information
  Misspeculation rates are relatively low
  With re-order buffer or checkpointing

## Slide 21: Speculative Page Table Walk
TLB miss
Page walks with flat nested page table
Speculative page walk
with inverted shadow page table
Speculative execution
Retired ?
2
4
6
8
gCR3
gVA
nCR3
sPA
3
5
1
7
9
sPA*: Speculatively obtained system physical address
gVA
sPA*
1
PID
VMID

## Slide 22: Experimental Methodology
Simics with custom memory hierarchy model
  Processor
    Single in-order processor for x86
  Cache
    Split L1 I/D and unified L2
  TLB
    Split L1 I/D and L2 I/D
  Page Walk Cache
    intermediate translations
  Nested TLB
    guest physical to system physical translation
Xen hypervisor on Simics
  Domain-0 and Domain-U(guest VM) are running
Workloads (more in the paper)
  SPECint 2006: Gcc, mcf, sjeng
  Commercial: SPECjbb, RUBiS, OLTP likes

## Slide 23: Evaluated Schemes
State-of-the-art hardware 2D page walker (base)
  With 2D PWC and NTLB
  [Bhargava et al. ASPLOS ’08]
Flat nested walker (flat)
  With 1D PWC and NTLB
Speculative inverted shadow paging (SpecISP)
  With flat nested page tables as backing page tables
Perfect TLB

## Slide 24: Performance Improvements
Chart: Normalized runtime (%)
| gcc | mcf | sjeng | SPECjbb | RUBiS | OLTP | OrderEntry | Volano
base | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
flat (w/ 1D_PWC + NTLB)
SpecISP (w/ flat)
Perfect-TLB
Better
[SPECint]
[Commercial]

## Slide 25: Performance Improvements
Chart: Normalized runtime (%)
| gcc | mcf | sjeng | SPECjbb | RUBiS | OLTP | OrderEntry | Volano
base | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
flat (w/ 1D_PWC + NTLB) | 93.0682 | 95.1952 | 94.1877 | 94.3228 | 90.5674 | 91.1531 | 91.5154 | 88.0653
SpecISP (w/ flat)
Perfect-TLB
[SPECint]
[Commercial]

## Slide 26: Performance Improvements
Chart: Normalized runtime (%)
| gcc | mcf | sjeng | SPECjbb | RUBiS | OLTP | OrderEntry | Volano
base | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
flat (w/ 1D_PWC + NTLB) | 93.0682 | 95.1952 | 94.1877 | 94.3228 | 90.5674 | 91.1531 | 91.5154 | 88.0653
SpecISP (w/ flat) | 85.0245 | 86.9757 | 87.211 | 89.927 | 80.9311 | 83.9998 | 83.4697 | 74.4876
Perfect-TLB
[SPECint]
[Commercial]

## Slide 27: Performance Improvements
Up to 25%(Volano), Average 14%
Chart: Normalized runtime (%)
| gcc | mcf | sjeng | SPECjbb | RUBiS | OLTP | OrderEntry | Volano
base | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
flat (w/ 1D_PWC + NTLB) | 93.0682 | 95.1952 | 94.1877 | 94.3228 | 90.5674 | 91.1531 | 91.5154 | 88.0653
SpecISP (w/ flat) | 85.0245 | 86.9757 | 87.211 | 89.927 | 80.9311 | 83.9998 | 83.4697 | 74.4876
Perfect-TLB | 80.2738 | 82.1901 | 83.2983 | 84.3924 | 73.4795 | 75.0358 | 74.6353 | 67.1614

## Slide 28: Conclusions
Our paper is revisiting the page walks for virtualized systems
  Differences of memory managements for virtual machines and for processes in native systems
We propose a bottom-up reorganization of address translation supports for virtualized systems
  Flattening nested page tables
    Reduce memory references for 2D page walks with little extra hardware
  Speculative inverted shadow paging
    Reduce the cost of a nested page walk

## Slide 29: Thank you ! Revisiting Hardware-Assisted Page Walks for Virtualized Systems
Jeongseob Ahn, Seongwook Jin, and Jaehyuk Huh
Computer Science Department
KAIST

## Slide 30: Backup Slides

## Slide 31: Details on SpecISP
Cumulative distributions of TLB miss latencies
Misspeculation rates
workloads | Mis-spec. rate | workloads | Mis-spec. rate
gcc | 2.072% | SPECjbb | 0.057%
mcf | 0.008% | Volano | ≈ 0.000%
sjeng | 0.150% | KernelCompile | 5.312%
Volano
90 cycles
CDF
Penalty: misspeculation << hypervisor intervention

## Slide 32: Details on SpecISP
Cumulative distributions of TLB miss latencies
Misspeculation rates
workloads | Mis-spec. rate | workloads | Mis-spec. rate
gcc | 2.072% | SPECjbb | 0.057%
mcf | 0.008% | Volano | ≈ 0.000%
sjeng | 0.150% | KernelCompile | 5.312%
Volano
90 cycles
CDF
Penalty: misspeculation << hypervisor intervention
Chart: Normalized runtime (%)
| KernelCompile | Volano
base | 100 | 100
flat (w/ 1D_PWC + NTLB) | 95.6725 | 88.0653
SpecISP (w/ flat) | 91.7534 | 74.4876
Perfect-TLB | 88.0814 | 67.1614