## Slide 1: Micro-sliced Virtual Processors to Hide the Effect of Discontinuous CPU Availability for Consolidated Systems
Jeongseob Ahn, Chang Hyun Park, and Jaehyuk Huh
Computer Science Department
KAIST

## Slide 2: Virtual Time Discontinuity
vCPU 1
Virtual time
Physical time
pCPU 0
vCPU 0
Time slice
Context Switching
Virtual CPUs are not always running
Time shared

## Slide 3: Interrupt with Virtualization
vCPU 0
pCPU 0
Interrupt
Interrupt occurs on vCPU0
vCPU 1
Interrupt processing is delayed
T
Interrupt
Delay

## Slide 4: Spinlock with Virtualization
vCPU 1
pCPU 0
vCPU 0
vCPU0 holding a lock is preempted
vCPU1 starts spinning to acquire the lock
T
vCPU0 releases the lock next time
Lock acquiring is delayed
Delay

## Slide 5: Prior Efforts in Hypervisor
Highly focused on modifying the hypervisor case by case
Hypervisor
Parallel
workload
Web
server
HPC
workload
Spinlock
optimization
Other
optimization
I/O interrupt
optimization
Memory
CPUs
I/O
  Spin detection buffer [Wells et al. PACT ‘06]
  Relaxed co-scheduling [VMware ESX]
  Balanced scheduling [Sukwong and Kim, EuroSys ’11]
  Preemption delay [Kim et al. ASPLOS ‘13]
  Preemptable spinlock [Ouyang and Lange, VEE ‘13]
  Boosting I/O requests [Ongaro et al. VEE ’08]
  Task-aware VM scheduling [Kim et al. VEE ‘09]
  vSlicer [Xu et al. HPDC ‘12]
  vTurbo [Xu et al. USENIX ATC ‘13]
Keep your hypervisor simple

## Slide 6: Fundamental of CPU Scheduling
Most of the CPU schedulers employ time-sharing
vCPU 1
pCPU 0
vCPU 0
vCPU 2
Turn around time
Time slice
T

## Slide 7: Toward Virtual Time Continuity
To minimize the turn around time, we propose shorter but more frequent runs
vCPU 1
pCPU 0
vCPU 0
vCPU 2
Shortened time slice
Reduced turn around time
T

## Slide 8: Methodology for Real System
4 physical CPUs (Intel Xeon)
  Xen hypervisor 4.2.3
  2 VMs
    4 vCPUs, 4GB memory
    Ubuntu 12.04 HVM
    Linux kernel 3.4.35
  1G network
Benchmarking workloads
  PARSEC (Spinlock and IPI)*
  iPerf (I/O interrupt)
  SPEC-CPU 2006
Xen Hypervisor
OS
App
OS
App
4 physical CPUs
4 virtualized
CPUs
2-to-1 consolidation ratio
*[Kim et al., ASPLOS ‘13]

## Slide 9: PARSEC Multi-threaded Applications
Co-running with Swaptions
Xen default: 30ms time slice
*Other PARSEC results in our paper
Better
Chart: Throughput increases (%)
| blacksc. | bodytr. | canneal | dedup | facesim | ferret | fluid. | freqmine | raytrace | stream. | vips | x264
10ms | 0.83066 | 12.4506 | 26.8125 | -4.7856 | 9.0076 | 16.2638 | 13.0455 | -2.4711 | 4.5388 | 5.8388 | 17.2342 | -1.5768
5ms | 0.14859 | 28.1291 | 31.8036 | 5.8215 | 16.9882 | 14.2442 | 17.8207 | -1.1574 | 9.105 | 16.8243 | 33.643 | -18.0991
1ms | -2.8489 | 30.0428 | 37.7634 | 13.9105 | 13.0902 | 13.8362 | 23.2206 | -2.3368 | 11.0552 | 17.829 | 53.303 | -25.0538
0.1ms
Chart: 
| blacksc. | bodytr. | canneal | dedup | facesim | ferret | fluid. | freqmine | raytrace | stream. | vips | x264
10ms
5ms
1ms
0.1ms | -9.8241 | 0.62853 | 13.3501 | 59.3943 | -7.5999 | 2.891 | 15.154 | -15.3891 | 0.5285 | -11.0281 | 29.0841 | -49.2647
-49

## Slide 10: Mixed VM Scenario*
Evaluate a consolidated scenario of I/O intensive and multi-threaded workloads
iPerf
 | VM1 | VM2 | VM3 | VM4
workloads | ferret(m), iPerf(I/O) | vips(m) | Dedup(m) | 3 x swaptions(s), streamcluster(s)
Parsec
* [vTurbo, USENIX ATC ‘13], [vSlicer, HPDC ’12], [Task-aware, VEE ‘09]
Chart: Throughput (Mbits/sec)
| 30ms | 1ms | 0.1ms
Throughput | 318.91 | 664.23 | 934.85
Jitters
Chart: 
| 30ms | 1ms | 0.1ms
Throughput
Jitters | 5.83 | 1.23 | 0.25
ferret: 1.7x
vips: 1.9x
dedup: 2.3x
In 1ms time slice

## Slide 11: SPEC Single-threaded Applications
SPEC CPU 2006 with Libquantum
*Page coloring technique is used to isolate cache
Xen default: 30ms time slice
Shortening the time slice provides a generalized solution but has the overhead of frequent context switching
Better
Chart: Normalized runtime (%)
| bzip2 | gcc | mcf | sjeng | h264ref | omnetpp | astar | xalancbmk | milc | cactusADM | lelie3d | namd | soplex | povray | GemsFDTD | lbm
1ms | 142.86 | 124.37 | 109.66 | 112.99 | 111.93 | 127.91 | 116.44 | 125.38 | 104.08 | 105.34 | 107.35 | 106.72 | 114.63 | 110.92 | 107.44 | 109.57
1ms w/ cache isolation*
Chart: 
| bzip2 | gcc | mcf | sjeng | h264ref | omnetpp | astar | xalancbmk | milc | cactusADM | lelie3d | namd | soplex | povray | GemsFDTD | lbm
1ms
1ms w/ cache isolation* | 115.65 | 112.34 | 105.68 | 102.6 | 102.27 | 118.6 | 105.48 | 114.26 | 102.72 | 103.05 | 106.62 | 101.68 | 109.18 | 102.64 | 105.79 | 105.22

## Slide 12: Overheads of Short Time Slice
vCPU 1
vCPU 0
pCPU 0
Frequent context switching
Pollution of architectural structures
T
$
$
$
Notes: The overheads of short time slice consist of two factors.
First (Click) is the increased number of context switching.
Second factor (Click) is the pollution of architectural structures such as Caches and TLBs. When you multiplex virtual CPUs at a high frequency, the architectural structures can be quickly polluted. As I mentioned in the previous slide, cache sensitive applications will be hurt by the cache sharing effects.

## Slide 13: Methodology for Simulated System
We use MARSSx86 full-system simulator with DRAMSim2
  Modified Linux scheduler to simulate 30ms and 1ms time slices
  Executed mixes of two applications on a single CPU
  Used SPEC-CPU 2006 applications
System configurations | 
Processor | Out-of-order x86 (Xeon)
L1 I/D Cache | 32KB, 4-way, 64B
L2 Cache | 256KB, 8-way, 64B
L3 Cache | 2MB, 16-way, 64B
Memory | DDR3-1600, 800Mhz
CPU: fits in L2 cache
CFR: cache friendly
THR: cache thrashing

## Slide 14: Performance Effects of Short Time Slice
Chart: Normalized CPI (%)
| omnetpp | gcc | astar | xalancbmk | bzip2 | soplex | gcc | libquantum | bzip2 | libquantum | omnetpp | libquantum | astar | libquantum | xalancbmk | libquantum | Mix9 | Mix10 | Mix11 | Mix12 | Mix13 | Mix14 | Mix15 | Mix16
30ms | 53.06 | 73.22 | 73.22 | 95.9 | 95.06 | 57.41 | 73.67 | 32.99 | 95.07 | 33.07 | 53.13 | 32.83 | 95.58 | 32.89 | 95.69 | 32.87
1ms | 53.7 | 74.67 | 74.67 | 99.33 | 95.85 | 57.75 | 74.45 | 32.91 | 95.88 | 32.98 | 53.64 | 32.92 | 95.32 | 32.94 | 99.77 | 32.96
Cache overheads (%) | 46.94 | 50.89 | 26.78 | 35.12 | 26.78 | 35.12 | 4.1 | 26.13 | 4.94 | 19.14 | 42.59 | 55.06 | 26.33 | 36.77 | 67.01 | 66.48 | 4.93 | 19.81 | 66.93 | 66.91 | 46.87 | 57.52 | 67.17 | 66.49 | 4.42 | 42.45 | 67.11 | 66.92 | 4.31 | 42.03 | 67.13 | 66.47
Type-4 (CFR – CFR)
Type-5 (CFR – THR)
142
30ms
1ms
CFR: cache friendly
THR: cache thrashing
Better

## Slide 15: Mitigating Cache Pollution
Context prefetcher [Daly and Cain, HPCA ‘12] [Zebchuk et al., HPCA ‘13]
  The evicted cache blocks of other VMs are logged
  When the VM is re-scheduled, the logged blocks will be prefetched
    May cause memory bandwidth saturation & congestion
Context preservation
  Retains the data of previous contexts with dynamic insertion policy* to either MRU or LRU position
Cache size
Perf.
Cache size
Perf.
MRU
LRU
Preserved
CFR: cache friendly
THR: cache thrashing
1ms
MRU
LRU
1ms
8ms
Winner of the two insertion policies
Simple time-sampling mechanism
* [Qureshi et al., ISCA ‘07]

## Slide 16: Evaluated Schemes
Configuration | Description
Baseline | 30ms time slice (Xen default)
1ms | 1ms time slice
1ms w/ ctx-prefetch* | State-of-the-art context prefetch
1ms w/ DIP | Dynamic insertion policy
1ms w/ DIP + ctx-prefetch | DIP with context prefetch
1ms w/ SIP-best | Optimal static insertion policy
* [Zebchuk et al., HPCA ‘13]

## Slide 17: Performance with Cache Preservation
Type 5 (CFR – THR)
Chart: Noramlized CPI (%)
| gcc | libquan. | bzip2 | libquan. | omnetpp | libquan. | astar | libquan. | xalan. | libquan. | Mix12 | Mix13 | Mix14 | Mix15 | Mix16
1ms | 111.22 | 99.39 | 115.69 | 99.89 | 111.16 | 99.41 | 137.77 | 99.86 | 141.8 | 99.43
1ms w/ ctx-prefetch
1ms w/ DIP
1ms w/ DIP + ctx-prefetch
1ms w/ SIP-best | 102.89 | 98.78 | 104.03 | 98.95 | 102.64 | 98.75 | 105.18 | 98.87 | 106.8 | 98.94
Chart: 
| gcc | libquan. | bzip2 | libquan. | omnetpp | libquan. | astar | libquan. | xalan. | libquan. | Mix12 | Mix13 | Mix14 | Mix15 | Mix16
1ms
1ms w/ ctx-prefetch | 109.95 | 98.58 | 115.28 | 99.22 | 110.78 | 98.92 | 132.89 | 99.25 | 122.91 | 99.81
1ms w/ DIP
1ms w/ DIP + ctx-prefetch
1ms w/ SIP-best
Chart: 
| gcc | libquan. | bzip2 | libquan. | omnetpp | libquan. | astar | libquan. | xalan. | libquan. | Mix12 | Mix13 | Mix14 | Mix15 | Mix16
1ms
1ms w/ ctx-prefetch
1ms w/ DIP | 100.85 | 98.88 | 108.12 | 99.04 | 107.86 | 99.07 | 109.72 | 99.08 | 116.93 | 99.06
1ms w/ DIP + ctx-prefetch
1ms w/ SIP-best
Chart: 
| gcc | libquan. | bzip2 | libquan. | omnetpp | libquan. | astar | libquan. | xalan. | libquan. | Mix12 | Mix13 | Mix14 | Mix15 | Mix16
1ms
1ms w/ ctx-prefetch
1ms w/ DIP
1ms w/ DIP + ctx-prefetch | 101.91 | 98.93 | 107.4 | 99.24 | 106.96 | 98.89 | 107.63 | 99.15 | 111.09 | 99.02
1ms w/ SIP-best
Better
CFR: cache friendly
THR: cache thrashing
142

## Slide 18: Performance with Cache Preservation
Type 4 (CFR – CFR)
Baseline: 30ms time slice
Chart: Noramlized CPI (%)
| omnetpp | gcc | astar | xalan. | bzip2 | soplex | Mix9 | Mix10 | Mix11
1ms | 104.59 | 109.79 | 115.91 | 125.46 | 114.99 | 112.81
1ms w/ ctx-prefetch | 104.75 | 109.13 | 118.08 | 120.98 | 114.79 | 113.12
1ms w/ DIP | 104.99 | 107.74 | 116.51 | 120.84 | 111.87 | 116.45
1ms w/ DIP + ctx-prefetch | 105.16 | 107.36 | 117.56 | 120.69 | 114.27 | 114.58
1ms w/ SIP-best | 102.36 | 104.79 | 113.92 | 118.07 | 113.99 | 112.37
CFR: cache friendly

## Slide 19: Conclusion
Investigated unexpected artifacts of CPU sharing in virtualized systems
  Spinlock and interrupt handling in kernel
Shortening time slice
  Improving runtime for PARSEC multi-threaded applications
  Improving throughput and latency for I/O applications
Context prefetcher with dynamic insertion policy
  Minimizing the negative effects of short time slice
  Improving performance for SPEC cache-sensitive applications

## Slide 20: Micro-sliced Virtual Processors to Hide the Effect of Discontinuous CPU Availability for Consolidated Systems
Jeongseob Ahn, Chang Hyun Park, and Jaehyuk Huh
Computer Science Department
KAIST