## Slide 1: Accelerating Critical OS Services in Virtualized Systems with Flexible Micro-sliced Cores
Jeongseob Ahn*, Chang Hyun Park‡, Taekyung Heo‡, Jaehyuk Huh‡
‡
*

## Slide 2: Challenge of Server Consolidation
Utilization
Fraction of time
0
1
0.5
Consolidation improves system utilization
However, resources are contended

## Slide 3: Challenge of Server Consolidation
Utilization
Fraction of time
0
1
0.5
Consolidation improves system utilization
However, resources are contended

## Slide 4: So, What Can Happen?
Virtual time discontinuity
vCPU 1
pCPU 0
vCPU 0
Physical Time
Virtual Time
Running
VMEXIT / VMENTER
Time shared
Waiting

## Slide 5: So, What Can Happen?
Virtual time discontinuity
vCPU 1
pCPU 0
vCPU 0
Physical Time
Virtual Time
Running
VMEXIT / VMENTER
Time shared
Waiting
Kernel Component | Avg. waiting time (μsec) | 
 | solo | co-run*
Page reclaim | 1.03 | 420.13
Page allocator | 3.42 | 1,053.26
Dentry | 2.93 | 1,298.87
Runqueue | 1.22 | 256.07
➊ Spinlock waiting time(gmake)
 |  | Avg. | Min. | Max.
dedup | solo | 28 | 5 | 1927
 | co-run* | 6,354 | 7 | 74915
vips | solo | 55 | 5 | 2052
 | co-run* | 14,928 | 17 | 121548
➋ TLB synchronization latency (μsec)
 | Jitters (ms) | Throughput (Mbits/sec)
solo | 0.0043 | 936.3
mixed co-run* | 9.2507 | 435.6
➌ I/O latency & throughput (iPerf)
Processing time is amplified
* Concurrently running with Swaptions of PARSEC

## Slide 6: How about Shortening Time Slice?
Waiting time
vCPU 1
pCPU 0
vCPU 0
vCPU 2
Time slice
T
Time shared
vCPU 1
pCPU 0
vCPU 0
vCPU 2
Reduced waiting time
T
Time shared
Shortening time slice is very simple and powerful, but the overhead of frequent context switches is significant

## Slide 7: Approach: Dividing CPUs into Two Pools
vCPU 1
vCPU 0
vCPU 2
Waiting time
Time slice
pCPU 0
Shortened time slice
pCPU 3
vCPU 1
vCPU 0
vCPU 2
➊ Normal pool
➋ Micro-sliced pool
Serving critical OS services to minimize the waiting time
- quickly but briefly schedule vCPUs
Serving the main work of applications

## Slide 8: Challenges in Serving Critical OS Services on Micro-sliced Cores
1. Precise detection of urgent tasks
2. Guest OS transparency
3. Dynamic adjustment of micro-sliced cores

## Slide 9: Detecting Critical OS Services
➊
Examining the instruction pointer (a.k.a PC)
whenever a vCPU yields its pCPU
Instruction pointer
workloads | # of yields | 
 | solo | co-run*
gmake | 79,440 | 295,262,662
exim | 157,023 | 24,102,495
dedup | 290,406 | 164,578,839
vips | 644,643 | 57,650,538
* Concurrently running with Swaptions of PARSEC
0x8106ed62

## Slide 10: Profiling Virtual CPU Scheduling Logs
Investigating frequently preempted regions
Kernel symbol tables
Module | Operation
sched | scheduler_ipi() resched_curr() …
mm | flush_tlb_all() get_page_from_freelist() …
irq | irq_enter() irq_exit() …
spinlock | __raw_spin_unlock() __raw_spin_unlock_irq() …
In our paper, you can find the table in details
Critical Guest OS Components
vCPU scheduling trace
(w/ Inst. Pointer)
Instruction pointer and kernel symbols enable to precisely detect vCPUs preempted while executing critical OS services without guest OS modification

## Slide 11: Accelerating Critical Sections
➋
➊
➊ Yield occurring
➋ Investigating the preempted vCPUs
➌ Scheduling the selected vCPU on the micro-sliced pool
P3
P2
P1
P0
➌

## Slide 12: Accelerating Critical TLB Synchronizations
➋
➊
➊ Yield occurring
➋ Investigating the preempted vCPUs
➌ Scheduling the selected vCPU on the micro-sliced pool
➍ Dynamically adjusting micro-sliced cores based on profiling
P3
P2
P1
P0
➌
➍

## Slide 13: Detecting Critical I/O Events
I/O handling consists of a chain of operations involving potentially multiple vCPUs
➋
vIRQ
➌
vIPI
➊pIRQ

## Slide 14: Experimental Environments
Testbed
  12 HW threads (Intel Xeon)
  2 VMs with 12 vCPUs for each
  Xen hypervisor 4.7
Benchmarking workloads
  dedup and vips from PARSEC
  exim and gmake from MOSBENCH
Pool configuration
  Normal: 30ms (Xen default)
  Micro-sliced: 0.1ms
Xen hypervisor
OS
App
OS
App
12 physical threads
12 virtual
CPUs
2-to-1 consolidation ratio

## Slide 15: Performance of Micro-sliced Cores
Chart: Norm. execution time (%)
| dedup (VM-1) | swaptions (VM-2) | vips (VM-1) | swaptions (VM-2) | gmake (VM-1) | swaptions (VM-2)
 | 0 | 0 | 0 | 0 | 0 | 0
baseline | 1 | 1 | 1 | 1 | 1 | 1
static-ideal | 0.29965 | 1.1442 | 0.83478 | 0.93116 | 0.60868 | 1.1918
dynamic
3
3
3
3
1
1
[Our schemes]
Chart: 
| dedup (VM-1) | swaptions (VM-2) | vips (VM-1) | swaptions (VM-2) | gmake (VM-1) | swaptions (VM-2)
 | 0 | 0 | 0 | 0 | 0 | 0
baseline
static
dynamic | 0.36658 | 1.1402 | 0.84643 | 0.94142 | 0.61771 | 1.1731

## Slide 16: Performance of Micro-sliced Cores
Chart: Norm. execution time (%)
| dedup (VM-1) | swaptions (VM-2) | vips (VM-1) | swaptions (VM-2) | gmake (VM-1) | swaptions (VM-2)
 | 0 | 0 | 0 | 0 | 0 | 0
baseline | 1 | 1 | 1 | 1 | 1 | 1
static-ideal | 0.29965 | 1.1442 | 0.83478 | 0.93116 | 0.60868 | 1.1918
dynamic
Chart: 
| dedup (VM-1) | swaptions (VM-2) | vips (VM-1) | swaptions (VM-2) | gmake (VM-1) | swaptions (VM-2)
 | 0 | 0 | 0 | 0 | 0 | 0
baseline
static
dynamic | 0.36658 | 1.1402 | 0.84643 | 0.94142 | 0.61771 | 1.1731
3
3
3
3
1
1
[Our schemes]
Chart: # of yield exceptions
| baseline | static-ideal | dynamic
exim-swaptions | 117979373 | 72299116 | 63528473
8% gap
Chart: Throughtput improvement
| baseline | static-ideal | dynamic
exim | 1 | 3.9014 | 4.5641
swaptions | 1 | 1.1 | 1.0729

## Slide 17: I/O Performance
 | Workloads
VM-1 | iPerf lookbusy
VM-2 | lookbusy
Chart: Bandwidth (Mbps)
| Baseline | micro-sliced
TCP | 441.3 | 665.3
UDP
Chart: jitters (ms)
| Baseline | micro-sliced
TCP
UDP | 8.82 | 0.03

## Slide 18: Conclusions
We introduced a new approach to mitigate the virtual time discontinuity problem
Three distinct contributions
  Precise detection of urgent tasks
  Guest OS transparency
  Dynamic adjustment of the micro-sliced cores
Overhead is very low for applications which do not frequently use OS services

## Slide 19: Thank You! jsahn@ajou.ac.kr
Accelerating Critical OS Services in Virtualized Systems with Flexible Micro-sliced Cores
Jeongseob Ahn*, Chang Hyun Park‡, Taekyung Heo‡, Jaehyuk Huh‡
‡
*